## Slide 1
CFD
AN OVERVIEW OF VOF METHOD IN COMPUTATIONAL FLUID DYNAMICS
Presented by :
Dharmansh Vyas
Arnav Maitreya
Jahnvi Soni

## Slide 2
MULTIPHASE FLOW
In fluid mechanics, multiphase flow is the simultaneous flow of materials with two or more thermodynamic phases.
  Method to solve
2. Eulerian-Eulerian Model
Treats each phase as an interpenetrating continuum, solving separate sets of conservation equations (mass, momentum, and energy) for each phase.
3. Eulerian-Lagrangian Model
Models the continuous phase using Eulerian framework and the dispersed phase using Lagrangian framework, tracking individual particles or droplets.
1. Volume of Fluid (VOF) Method
VOF is used to track the interface between immiscible fluids by solving a transport equation for the volume fraction of one of the fluids.
There are other ways too to solve multiphase flow

## Slide 3
  Definition: The Volume of Flow Method (VOF) is a numerical technique used in CFD to track and locate the free surface (or interface) between two immiscible fluids.
  Principles: VOF is based on the concept of a fractional volume of fluid (vof) within each computational cell.
  Difference: Unlike other methods like Finite Volume Method (FVM) or Finite Element Method (FEM), VOF focuses specifically on capturing the dynamics of the interface between fluids.
  The VOF method utilizes the transport equation to handle the distribution and movement of the fluid phases. Here’s a detailed explanation of how the transport equation is related to the VOF method:
  The VOF method uses a fractional volume function, F, to represent the volume fraction of one of the fluids within each computational cell. The value of F ranges from 0 to 1, where:
  F=0: The cell is entirely filled with the second fluid.
  F=1: The cell is entirely filled with the first fluid.
  0<F<1: The cell contains the interface between the two fluids.

## Slide 6
Transport Equation
Convective term gives us idea that how the scalar is changing by the flow of the fluid.
Diffusion term tell us ,how the scalar diffuses in the fluid.
The source term, represents the amount of the scalar quantity created or destroyed inside the control volume.
Unsteady term represents the change of scalar w.r.t time.

## Slide 7
Transport Equation in VOF Method

## Slide 8
The physical properties (e.g., density ρ and viscosity μ) of the fluid mixture are computed as weighted averages based on the volume fraction F:

## Slide 9
Laminar Flow
  Problem -1 (Lid-Driven Cavity)
the flow will be assumed laminar and will be solved on a uniform mesh using the icoFoam solver for laminar, isothermal, incompressible flow.

## Slide 10
  movingWall -(wall)
(3 7 6 2)
  fixedWalls -(Wall)
(0 4 7 3)
(2 6 5 1)
(1 5 4 0)
  frontAndBack-(Empty)
(0 3 2 1)
(4 5 6 7)
  Computational Domain

## Slide 11
blocks
(
hex (0 1 2 3 4 5 6 7) (100 100 1) simpleGrading (1 1 1)
);
100 x 100
  Type of mesh
The computational mesh is a structured, uniform, rectangular grid.
The grid is discretized into a finite number of cells. The domain is divided into 100 cells along the x-axis and 100 cells along the y-axis with only 1 cell in z- direction.

## Slide 12
  movingWall -(wall)
(3 7 6 2)
  fixedWalls -(Wall)
(0 4 7 3)
(2 6 5 1)
(1 5 4 0)
  frontAndBack-(Empty)
(0 3 2 1)
(4 5 6 7)
  movingWall -(wall)
Zero Gradient
  fixedWalls -(Wall)
Zero Gradient
  frontAndBack-(Empty)
empty
INFERENCE- there is no pressure difference along thier length
  movingWall -(wall)
fixedValue (1 0 0)
INFERENCE- the velocity field have value of 1 in x direction
  fixedWalls -(Wall)
no Slip
INFERENCE- The velocity of the fluid in contact with the wall is zero.
  frontAndBack-(Empty)
empty
internalField uniform (0 0 0);
INFERENCE- Initially, the velocity inside the domain is zero.
  Boundary and initial Conditions
Pressue
Velocity

## Slide 13
  Result
1. Velocity Field:
  Formation of a primary vortex due to moving lid and secondary vortices near stationaly corners.
2. Pressure Field :
  Higher pressure at the lower right corner and lower pressure at the upper left corner.
3. Streamlines :
  Visualization of flow paths within the cavity . Clear indication of vortex structure.

## Slide 14
  Result

## Slide 15
Laminar Flow
  Problem -2 (Skewed Lid-Driven Skew Cavity)
the flow will be assumed laminar and will be solved on a uniform mesh using the icoFoam solver for laminar, isothermal, incompressible flow.

## Slide 16
  movingWall -(wall)
(3 7 6 2)
  fixedWalls -(Wall)
(0 4 7 3)
(2 6 5 1)
(1 5 4 0)
  frontAndBack-(Empty)
(0 3 2 1)
(4 5 6 7)
  Computational Domain

## Slide 17
blocks
(
hex (0 1 2 3 4 5 6 7) (100 100 1) simpleGrading (1 1 1)
);
100 x 100
  Type of mesh
The computational mesh is a structured, uniform, skewed grid at 60 degrees.
The grid is discretized into a finite number of cells. The domain is divided into 100 cells along the x-axis and 100 cells along the y-axis with only 1 cell in z- direction.

## Slide 18
  movingWall -(wall)
(3 7 6 2)
  fixedWalls -(Wall)
(0 4 7 3)
(2 6 5 1)
(1 5 4 0)
  frontAndBack-(Empty)
(0 3 2 1)
(4 5 6 7)
  movingWall -(wall)
Zero Gradient
  fixedWalls -(Wall)
Zero Gradient
  frontAndBack-(Empty)
empty
INFERENCE- there is no pressure difference along thier length
  movingWall -(wall)
fixedValue (1 0 0)
INFERENCE- the velocity field have value of 1 in x direction
  fixedWalls -(Wall)
no Slip
INFERENCE- The velocity of the fluid in contact with the wall is zero.
  frontAndBack-(Empty)
empty
internalField uniform (0 0 0);
INFERENCE- Initially, the velocity inside the domain is zero.
  Boundary and initial Conditions
Pressue
Velocity

## Slide 19
  Result
1. Velocity Field:
  Skewed primary vortex, possible secondary vortices near corners, and altered velocity vectors and contours.
2. Pressure Field :
  Adjusted high-pressure regions and shifted zones influenced by 60-degree skewness.
3. Streamlines :
  Skewed flow paths reflecting the inclination. Clear depiction of skewed vortex structures.

## Slide 20
  Result

## Slide 21
Laminar Flow
  Problem -3 (elbow)
The elbow tutorial in OpenFOAM provides a comprehensive example of setting up, running, and post-processing a steady-state incompressible turbulent flow simulation in a curved pipe.

## Slide 22
  Inlet 1
( 9 10 11 12 )
  Inlet 2
(5 6 7 8 )
  Outlet
(1 2 3 4 )
  Fixed wall Upper
(10 1 4 11)
  Fixed wall Lower
(9 2 3 12)
  Computational Domain
1
2
5
3
4
6
8
7
12
9
11
10

## Slide 23
  Type of mesh
  The computational mesh is an unstructured, non-uniform, triangular mesh.
  With inlets having nFaces 8 and 4, outlet with 8 and walls having 34 and 100.
  Mesh is generated using Fluent with .msh extension and then converted in openFoam format with “fluentToFoam” command.

## Slide 24
  Inlet 1
Zero Gradient
  Inlet 2
Zero Gradient
  Fixed wall Upper
Zero Gradient
  Fixed wall Lower
Zero Gradient
INFERENCE- there is no pressure difference along thier length
  frontAndBack-(Empty)
empty
  outlet
Fixed Value
INFERENCE- the pressure at the outlet of the computational domain is set to a constant value, which is crucial for driving the flow through the elbow.
  Boundary and initial Conditions
Pressue
Velocity
  Inlet 1
( 9 10 11 12 )
  Inlet 2
(5 6 7 8 )
  Outlet
(1 2 3 4 )
  Fixed wall Upper
(10 1 4 11)
  Fixed wall Lower
(9 2 3 12)
  Inlet 1
fixed Value - uniform(1 0 0)
INFERENCE- the velocity filed at inlet 2 with 1m/s in x direction
  Inlet 2
fixed Value - uniform(0 3 0)
INFERENCE- the velocity filed at inlet 1 with 3m/s in y direction
  Fixed wall Upper
no slip
  Fixed wall Lower
no slip
  frontAndBack-(Empty)
empty
  outlet
Zero Gradient

## Slide 25
  Result
  Velocity Fields :
  Inlets show smooth and uniform velocity due to zeroGradient, ensuring consistent flow entry.
2. Pressure Fields :
  Outlets maintain constant pressure via fixedValue, ensuring controlled pressure.
  Pressure drop along the elbow, typical for fluid flow through curves.

## Slide 26
  Result

## Slide 27
VOF METHOD
  Problem -4 (Dam-break)
The test setup consists of a column of water at rest located behind a membrane on the left side of a tank. At time t = 0 s , the membrane is removed and the column of water collapses. During the collapse, the water impacts an obstacle at the bottom of the tank and creates a complicated flow structure, including several captured pockets of air.
Our goal is to study that complicated structure.

## Slide 28
  left Wall
(0 12 16 4)
(4 16 20 8)
  right Wall
(7 19 15 3)
(11 23 19 7)
  lower Wall
(0 1 13 12)
(1 5 17 13)
(5 6 18 17)
(2 14 18 6)
(2 3 15 14)
  atmosphere
(8 20 21 9)
(9 21 22 10)
(10 22 23 11)
  Computational Domain

## Slide 29
  Type of mesh
The computational mesh is structured,regular ,rectangular grids.
The Domain is divided into 5 blocks each having finite no. of cells.
blocks
(
hex (0 1 5 4 12 13 17 16) (23 8 1) simpleGrading (1 1 1)
hex (2 3 7 6 14 15 19 18) (19 8 1) simpleGrading (1 1 1)
hex (4 5 9 8 16 17 21 20) (23 42 1) simpleGrading (1 1 1)
hex (5 6 10 9 17 18 22 21) (4 42 1) simpleGrading (1 1 1)
hex (6 7 11 10 18 19 23 22) (19 42 1) simpleGrading (1 1 1)
);

## Slide 30
  Boundary and initial Conditions
Pressue
  leftWall
fixedFluxPressure - uniform 0
  rightWall
fixedFluxPressure - uniform 0
  lowerWall
fixedFluxPressure - uniform 0
INFERENCE- The flux is specified at the boundary, and pressure is adjusted to maintain this flux.
  atmosphere
totalPressure - uniform 0
  defaultFaces
empty
Velocity
alpha.water
  leftWall
noSlip
  rightWall
noslip
  lowerWall
noSlip
INFERENCE- velocity at wall is 0
  atmosphere
pressureInletOutletVelocit
- uniform (0 0 0)
iNFERENCE-
  defaultFaces
empty
internal Field uniform 0
  leftWall
zeroGradient
  rightWall
zeroGradient
  lowerWall
zeroGradient
  atmosphere
inletOutlet
inlet - uniform 0
iNFERENCE-
  defaultFaces
empty

## Slide 31
  Initial Set Fields :
value of volume fraction(f) or alpha, is set by taking primary fluid as water and secondary fluid as air.
f = 1 (water) f = 0 (air)
defaultFieldValues
(
volScalarFieldValue alpha.water 0
);
// domain is field with air as f = 0, region is shown by blue.
regions
( boxToCell
{ box (0 0 -1) (0.1461 0.292 1);
fieldValues
( volScalarFieldValue alpha.water 1
); } );
// columne of water is at initial condition is set in region having f =1, region shown by red color.

## Slide 32
  Result
1.Early Collapse Phase:
  Water spreads out, forming a complex interface.
  High-velocity jet forms, leading to horizontal spread.
2.Impact on Walls:
  Jet impacts the opposite wall, causing splashes and secondary flows.
  Air pockets and mixing regions form near the impact site.

## Slide 33
  Result

## Slide 34
Pressure inside
water drop
=0.5445 N/m^2

## Slide 35
Pressure outside
water drop
= 0(approx)

## Slide 36
  theoretically pressure difference =
2*Sigma/r
=2*(0.072)*(0.25)
=0.576 N/m^2
  Computational result pressure difference =
=0.5445 N/m^2
  Error = 0.0315
  Error % = 3.15%
r=0.25m